Copyright 2020 by The American Institute of Architects (AIA)

Exclusively published and distributed by Deltek, Inc. for the AIA

This Product MasterSpec Section is licensed by Deltek, Inc. to Activar Construction Products Group, Inc. - JL Industries ("Licensee").

This independent Product MasterSpec section uses original MasterSpec text.

Revisions made to the original MasterSpec text are made solely by the Licensee and are not endorsed by, or representative of the opinions of, Deltek or The American Institute of Architects (AIA). Neither AIA nor Deltek are liable in any way for such revisions or for the use of this Product MasterSpec Section by any end user. A qualified design professional should review and edit the document to suit project requirements.

For more information, contact Activar Construction Products Group, Inc. - JL Industries, 9702 Newton Ave. S., Bloomington, MN 55431; Phone (800) 554-6077; Website: www.activarcpg.com; Email: sales@activarcpg.com.

For information about MasterSpec, contact Deltek at (800) 424-5080 or visit masterspec.com.

SECTION 104300 - EMERGENCY AID SPECIALTIES

TIPS:

To view non-printing Editor's Notes that provide guidance for editing, click on MasterWorks/Single-File Formatting/Toggle/Editor's Notes.

To read detailed research, technical information about products and materials, and coordination checklists, click on MasterWorks/Supporting Information.

Access Product MasterSpec Sections:

<Double click here to view the list of manufacturer Sections available at ProductMasterSpec.com.>

Revise this Section by deleting and inserting text to meet Project-specific requirements.

GENERAL

SUMMARY

Section includes:

Automated external defibrillator (AED).

Automated external defibrillator (AED) cabinet.

ALLOWANCES

Retain products and Work included in this Section that are covered by cash or quantity allowance. Do not include amounts. Insert descriptions of items in Part 2 or 3 to provide information affecting the cost of the Work that is not included under the allowance.

Automated external defibrillators are part of <Insert name of allowance>.

Automated external defibrillator cabinets are part of <Insert name of allowance>.

ACTION SUBMITTALS

Product Data: For each type of product.

Product Schedule: For automated external defibrillator cabinets. Coordinate final automated external defibrillator cabinet schedule with number and type of automated external defibrillators to ensure proper fit and function.[ Use same designations indicated on Drawings.]

Sustainable Design Submittals:

Retain "Product Data" Subparagraph below to require minimum recycled content for LEED 2009 MR Credit 4 - "Recycled Content."

Product Data: For recycled content, indicating postconsumer and preconsumer recycled content and cost.

Environmental product declaration.

"Product Certificates" Subparagraph below applies to LEED 2009, Materials and Resources Credit 5, "Regional Materials."

Product Certificates: For regional materials, indicating location of material manufacturer and point of extraction, harvest, or recovery for each raw material. Include distance to Project and cost for each regional material.

Retain "Environmental Product Declaration (EPD)" Subparagraph below for LEED v4 "MRc Building Product Disclosure and Optimization - Environmental Product Declarations." See the Evaluations. Verify, with manufacturer, that EPDs are available for each product.

Environmental Product Declaration (EPD): For each product.

"Product Certificates" Subparagraph below applies to IgCC, which requires that a minimum of 55 percent of building materials or products be extracted, harvested, manufactured, or recovered within 500 miles (800 km) of Project. See IgCC-2012, 505.2.5.

Product Certificates: For indigenous materials, indicating location of material manufacturer and point of extraction, harvest, or recovery for each raw material. Include distance to Project, means of transportation, and cost for each indigenous material.

Retain "Environmental Product Declaration" Subparagraph below if products specified in the Section are required to have an EPD to meet the IgCC's requirement of 55 percent recycled materials.

Environmental Product Declaration: For each product.

"Product Certificates" Subparagraph below applies to ASHRAE 189.1, which requires that a minimum of 15 percent of building materials or products be extracted, harvested, manufactured, or recovered within 500 miles (800 km) of Project. See ASHRAE 189.1-2014, 9.4.1.2.

Product Certificates: For regional materials, indicating location of material manufacturer and point of extraction, harvest, or recovery for each raw material. Include distance to Project, means of transportation, and cost for each regional material.

"Environmental Product Declaration" Subparagraph below applies to ASHRAE 189.1 if products specified in the Section are used to meet the requirements of paragraph 9.4.1.4, "Multiple-Attribute Product Declaration or Certification," which requires EPDs for a minimum of 10 products.

Environmental Product Declaration: For each product.

Subparagraphs below apply to Green Globes v1.4  if products specified in the Section are used to meet the requirements of paragraph 3.5.1.2 "Path B: Prescriptive Path for Building Core and Shell" -which requires that a certain percentage of the materials used in the core and shell have EPDs, third-party certifications, and/or third-party life cycle assessments.

Environmental Product Declaration: For each product.

Third-Party Certifications: For each product.

Third-Party Certified Life Cycle Assessment: For each product.

INFORMATIONAL SUBMITTALS

Warranty: Sample of special warranty.

CLOSEOUT SUBMITTALS

Operation and Maintenance Data: For automated external defibrillators and automated external defibrillator cabinets to include in maintenance manuals.

COORDINATION

Coordinate size of automated external defibrillator cabinets to ensure that type and capacity of automated external defibrillators indicated are accommodated.

Coordinate sizes and locations of automated external defibrillator cabinets with wall depths.

WARRANTY

When warranties are required, verify with Owner's counsel that special warranties stated in this article are not less than remedies available to Owner under prevailing local laws.

Special Warranty: Manufacturer's standard form in which manufacturer agrees to repair or replace automated external defibrillators that fail in materials or workmanship within specified warranty period.

Verify available warranties and warranty periods for automated external defibrillators with manufacturers.

Retain first option in "Warranty Period" Subparagraph below with JL Industries "LIFEPAK CR2 Defibrillator"; retain second option with "HeartSine Samaritan PAD 350P" model.

Warranty Period: [8] [10] years from date of Substantial Completion.

PRODUCTS

Manufacturers and products listed in this Section are neither recommended nor endorsed by the AIA or Deltek. Before selecting manufacturers and products, verify availability, suitability for intended applications, and compliance with minimum performance requirements. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

Product options commonly available from manufacturers are included in square brackets throughout the Section Text. Not every manufacturer listed can provide every option offered; verify availability with manufacturers. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

MANUFACTURERS

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturer's listed.

Basis-of-Design Product: Subject to compliance with requirements, provide Basis-of-Design products by Activar Construction Products Group, Inc. - JL Industries or comparable product by one of the following:

Automated External Defibrillator (AED):

HeartSine.

Philips.

Physio-Control.

<Insert manufacturer's name>.

Automated External Defibrillator (AED) Cabinets:

Modern Metal Products.

Safety Technology, Inc.

<Insert manufacturer's name>.

AUTOMATED EXTERNAL DEFIBRILLATOR (AED)

Retain first option in "Automated External Defibrillator" Paragraph below with JL Industries "HeartSine Samaritan PAD 350P"; retain second option with "LIFEPAK CR2 Defibrillator" model.

Visit http://www.activarcpg.com/jl-industries/emergency-specialties for additional product information.

Automated External Defibrillator: Portable automated external defibrillator capable of automatically diagnosing life-threatening cardiac arrhythmias, suitable for use on adult or pediatric patients. [Audible and visual with illuminated display icons] [Lid release, on/off button] operation. Type, size, and capacity for each [cabinet] indicated.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

JL Industries is an authorized reseller of the HeartSine and LIFEPAK emergency aid specialties indicated.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Activar Construction Products Group, Inc. - JL Industries; [HeartSine Samaritan PAD 350P] [LIFEPAK CR2 Defibrillator] or comparable product.

Retain first option in "Model" Subparagraph below with JL Industries "HeartSine Samaritan PAD 350P"; retain second, third, fourth, or fifth option with "LIFEPAK CR2 Defibrillator" model.

Model: [PAD] [LP-CR2-USB] [LP-CR2-USB-AUTO] [LP-CR2-WIFI] [LP-CR2-WIFI AUTO].

Storage Case: Manufacturer's standard.

Retain first option in "Battery Capacity" Paragraph below with JL Industries "HeartSine Samaritan PAD 350P"; retain second option with "LIFEPAK CR2 Defibrillator" model.

Battery Capacity: [6] [13] hours.

Retain first option in "Standby Life" Paragraph below with JL Industries "HeartSine Samaritan PAD 350P"; retain second option with "LIFEPAK CR2 Defibrillator" model.

Standby Life: [3.5] [6] years.

"Pediatric Pad-Pak" for patients 1 to 8 years or up to 55lb (25kg).

Optional Accessories: [Additional Adult Pad-Pak] [Pediatric Pad-Pak].

MOUNTABLE - AUTOMATED EXTERNAL DEFIBRILLATOR CABINET

Visit http://www.activarcpg.com/jl-industries/emergency-specialties for additional product information.

Automated External Defibrillator (AED) Cabinet Type: Mountable AED cabinet of suitable type, size and capacity for automated external defibrillator.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

JL Industries is an authorized reseller of the HeartSine and LIFEPAK emergency aid specialties indicated.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Activar Construction Products Group, Inc. - JL Industries; LifeStart cabinet product indicated or comparable product.

        - AED Cabinet Construction: Flush doors with 5/8-inch (15.88-mm) doorstop attached by continuous hinge and equipped with zinc-plated pull and roller catch.

Aluminum Steel Sheet Model: [1423] [1425] [1426] [1427].

Cold-Rolled Steel Sheet Model: [1413] [1415] [1416] [1417] [1419].

Stainless Steel Sheet Model: [1435] [1436] [1437] [1439].

Cabinet Construction: [Nonrated] [Two-hour fire rated].

Retain "Recessed Cabinet," "Semirecessed Cabinet," or "Surface-Mounted Cabinet" Paragraph below.

Recessed Cabinet: Exposed 3/8-inch (9.53-mm) Flat Trim: One-piece combination trim and perimeter door frame overlapping surrounding wall surface, with exposed trim face and wall return at outer edge (backbend).

Semirecessed Cabinet: One-piece combination trim and perimeter door frame overlapping surrounding wall surface, with exposed trim face and wall return at outer edge (backbend).

"Square-edge trim"  available with aluminum, steel or stainless steel doors; "rolled-edge trim" available with steel or stainless steel doors.

Square-Edge Trim: 1-1/2-inch (38-mm) backbend depth.

Rolled-Edge Trim: [2-1/2-inch (63-mm)] [3-inch (76-mm)] backbend depth.

Surface-Mounted Cabinet: [Square] [Rolled] edge cabinet box fully exposed and mounted directly on wall with no trim.

Door Glazing: Acrylic sheet.

Door Hardware: Manufacturer's standard door-operating hardware of proper type for cabinet type, trim style, and door material and style indicated.

Alarm: Alarm that actuates when fire-protection cabinet door is opened and that is powered by batteries.

Retain first option in "Basis-of-Design" Subparagraph below for JL Industries standard audible alarm; retain second option for JL Industries siren strobe model.

JL Industries is an authorized reseller of the HeartSine and LIFEPAK emergency aid specialties indicated.

Basis-of-Design: Activar Construction Products Group, Inc. - JL Industries; ["Commander," audible alarm or comparable] [Manufacturer's optional, siren strobe].

Alarm Contacts: [14MAG, Magnetic Door Contact] [14RR, Roller Reed Ball Contact] for existing alarm systems.

Identification: Manufacturer's standard graphics and lettering complying with authorities having jurisdiction for letter style, size, spacing, and location.

Door Finish:

Aluminum: Anodized, [Clear] [Dark Bronze].

Steel: Manufacturer's standard baked-enamel or powder coat finish.

Retain "Standard Color" Subparagraph below for JL Industries standard color; retain "Optional Colors" Subparagraph below for JL Industries optional color range. Verify availability of colors in "Optional Color" Subparagraph with manufacturer.

Standard Color: White.

Optional Colors: [AMS Beige] [Black] [Bronze] [Flat Black] [Gray] [Orange] [Red] [SC Beige] [Silver] [Yellow].

Stainless Steel: Manufacturer's standard #4 Satin.

FREESTANDING AUTOMATED EXTERNAL DEFIBRILLATOR CABINET

Visit http://www.activarcpg.com/jl-industries/emergency-specialties for additional product information.

Automated External Defibrillator (AED) Cabinet Type: Freestanding AED cabinet of suitable type, size, and capacity for automated external defibrillator.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

JL Industries is an authorized reseller of the HeartSine and LIFEPAK emergency aid specialties indicated.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Activar Construction Products Group, Inc. - JL Industries; Freestanding cabinet model indicated or comparable product.

        - AED Cabinet Construction: Flush doors with 5/8-inch (15.88-mm) doorstop attached by continuous hinge and equipped with zinc-plated pull and roller catch. 52-inch (1320-mm) high, inverted U-shaped stand of structural steel tubing with welded a steel base plate.

          - Aluminum Steel Sheet Model: 1483F12AL.

          - Cold-Rolled Steel Sheet Model: 1483F12.

Stainless Steel Sheet Model: 1483F12SS.

Alarm: Alarm that actuates when fire-protection cabinet door is opened and that is powered by batteries.

Retain first option in "Basis-of-Design" Subparagraph below for JL Industries standard audible alarm; retain second option for JL Industries siren strobe model.

          - Basis-of-Design: Activar Construction Products Group, Inc. - JL Industries; ["Commander," audible alarm or comparable] [Manufacturer's optional, siren strobe].

Alarm Contacts: [14MAG, Magnetic Door Contact] [14RR, Roller Reed Ball Contact] for existing alarm systems.

Door Finish:

Aluminum: Anodized, Clear.

Steel: Manufacturer's standard baked-enamel or powder coat finish.

Retain first option in "Color" Subparagraph below for JL Industries standard.

Color: [White] [Silver Metallic].

Stainless Steel: Manufacturers standard #4 Satin.

Door Glazing: Acrylic sheet, Clear.

Door Hardware: Manufacturer's standard door-operating hardware of proper type for cabinet type, trim style, and door material and style indicated.

Alarm: Alarm that actuates when fire-protection cabinet door is opened and that is powered by batteries.

Retain first option in "Basis-of-Design" Paragraph below for JL Industries standard audible alarm; retain second option for JL Industries siren strobe model.

JL Industries is an authorized reseller of the HeartSine and LIFEPAK emergency aid specialties indicated.

          - Basis-of-Design: Activar Construction Products Group, Inc. - JL Industries; ["Commander," audible alarm or comparable] [Manufacturer's optional, siren strobe].

Alarm Contacts: [14MAG, Magnetic Door Contact] [14RR, Roller Reed Ball Contact] for existing alarm systems.

Identification: Lettering complying with authorities having jurisdiction for letter style, size, spacing, and location. Locate as indicated by Architect.

DUAL AUTOMATED EXTERNAL DEFIBRILLATOR AND OXYGEN CABINET

Visit http://www.activarcpg.com/jl-industries/emergency-specialties for additional product information.

Automated External Defibrillator (AED) Cabinet Type: Mounted AED cabinet of suitable type, size and capacity for automated external defibrillator and oxygen.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

JL Industries is an authorized reseller of the HeartSine and LIFEPAK emergency aid specialties indicated.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Activar Construction Products Group, Inc. - JL Industries; Olympus Series- Dual AED and Emergency Oxygen cabinet product indicated or comparable product.

        - Dual-AED Cabinet Construction: Flush doors with 5/8-inch (15.88-mm) doorstop attached by continuous hinge and equipped with zinc-plated pull and roller catch.

Aluminum Steel Sheet Model: [1923] [1925] [1926] [1927].

Cold-Rolled Steel Sheet Model: [1913] [1915] [1916] [1917].

Stainless Steel Sheet Model: [1935] [1936] [1937] [1939].

Cabinet Construction: [Nonrated] [Two-hour fire rated].

Retain "Recessed Cabinet," "Semirecessed Cabinet," or "Surface-Mounted Cabinet" Paragraph below.

Recessed Cabinet: Exposed 3/8-inch (9.53-mm) Flat Trim: One-piece combination trim and perimeter door frame overlapping surrounding wall surface, with exposed trim face and wall return at outer edge (backbend).

Semirecessed Cabinet: One-piece combination trim and perimeter door frame overlapping surrounding wall surface, with exposed trim face and wall return at outer edge (backbend).

"Square-edge trim" is available with aluminum, steel, or stainless steel doors; "rolled-edge trim" is available with steel or stainless steel doors.

Square-Edge Trim: 1-1/2-inch (38-mm) backbend depth.

Rolled-Edge Trim: 3-inch (76-mm) backbend depth.

Retain first option in "Surface-Mounted Cabinet" Paragraph below for Dual-AED cabinet edges unless otherwise noted; retain second option with stainless steel model 1939.

Surface-Mounted Cabinet: [Square] [Rolled] edge cabinet box fully exposed and mounted directly on wall with no trim.

Oxygen: Accommodates up to "D" 16-1/2-inch (419-mm) size cylinder. Available with LIF-O-GEN® oxygen system that features an automatic flow system.

Door Glazing: Acrylic sheet, Clear.

Door Hardware: Manufacturer's standard door-operating hardware of proper type for cabinet type, trim style, and door material and style indicated.

Alarm: Alarm that actuates when fire-protection cabinet door is opened and that is powered by batteries.

Retain first option in "Basis-of-Design" Paragraph below for JL Industries standard audible alarm; retain second option for JL Industries siren strobe model.

          - Basis-of-Design: Activar Construction Products Group, Inc. - JL Industries; ["Commander," audible alarm or comparable] [Manufacturer's optional, Siren strobe].

Alarm Contacts: [14MAG, Magnetic Door Contact] [14RR, Roller Reed Ball Contact] for existing alarm systems.

Identification: Lettering complying with authorities having jurisdiction for letter style, size, spacing, and location. Locate as indicated by Architect.

Door Finish:

Aluminum: Anodized, [Clear] [Dark Bronze].

Steel: Manufacturer's standard baked-enamel or powder coat finish.

Retain first option in "Color" Subparagraph below for JL Industries standard color; select from remaining for available optional colors. Verify available with manufacturer.

Color: [White] [AMS Beige] [Black] [Bronze] [Flat Black] [Gray] [Orange] [Red] [SC Beige] [Silver] [Yellow].

Stainless Steel: Manufacturer's standard, #4 Satin.

WATER-RESISTANT - AUTOMATED EXTERNAL DEFIBRILLATOR CABINET

Visit http://www.activarcpg.com/jl-industries/emergency-specialties for additional product information.

Automated External Defibrillator (AED) Cabinet Type: Exterior mountable AED cabinet of suitable type, size and capacity for automated external defibrillator.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

JL Industries is an authorized reseller of the HeartSine and LIFEPAK emergency aid specialties indicated.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Activar Construction Products Group, Inc. - JL Industries; Water-Resistant Exterior cabinet Model indicated or comparable product.

        - AED Cabinet Construction: Tub and gasketed door constructed from fiberglass-reinforced polyester (FRP). Full-length stainless steel door hinge. Quick-opening latch.

JL Industries FRP AED cabinets feature UV-inhibited, halogen-free fiberglass.

Fiberglass-Reinforced Polyester Model:  1499.

Cabinet Construction: Nonrated.

Surface-Mounted Cabinet: Square edge cabinet box fully exposed and mounted directly on wall with no trim.

Door Glazing: Acrylic sheet, Clear.

Retain first option in "Door Hardware" Paragraph below for manufacturers standard.

Door Hardware: [Quick-opening latch] [Lockable latch with padlock hasp] door-operating hardware.

Optional Alarm: Manufacturer's standard [audible] [siren strobe] alarm that actuates when fire-protection cabinet door is opened and that is powered by batteries.

Retain first option in "Basis-of-Design" Subparagraph below for JL Industries standard audible alarm; retain second option for JL Industries siren strobe model.

          - Basis-of-Design: Activar Construction Products Group, Inc. - JL Industries; ["Commander," audible alarm or comparable] [Manufacturer's optional siren strobe].

Alarm Contacts: [14MAG, Magnetic Door Contact] [14RR, Roller Reed Ball Contact] for existing alarm systems.

Identification: [Die-Cut lettering] [Manufacturer's Standard Warning Decal].

Finish Color: White.

EXTERIOR - AUTOMATED EXTERNAL DEFIBRILLATOR CABINET

Visit http://www.activarcpg.com/jl-industries/emergency-specialties for additional product information.

Automated External Defibrillator (AED) Cabinet Type: Exterior mountable AED cabinet of suitable type, size and capacity for automated external defibrillator.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

JL Industries is an authorized reseller of the HeartSine and LIFEPAK emergency aid specialties indicated.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Activar Construction Products Group, Inc. - JL Industries; Exterior Surface Mount cabinet product indicated or comparable product.

        - AED Cabinet Construction: Tub and bulb-gasketed door constructed from galvannealed steel.Full-length stainless steel door hinge.

Galvannealed Steel Sheet Model:  1463.

Cabinet Construction: Nonrated.

Surface-Mounted Cabinet: Square edge cabinet box fully exposed and mounted directly on wall with no trim.

Door Glazing: Acrylic sheet, Clear.

Retain first option in "Door Hardward" Subparagraph below for JL Industries standard door hardware; retain second option to upgrade to keyed hardware.

Door Hardware: [Stainless steel turn handle] [Keyed-turn  turn handle].

Alarm: Alarm that actuates when fire-protection cabinet door is opened and that is powered by batteries.

Retain first option in "Basis-of-Design" Subparagraph below for JL Industries standard audible alarm; retain second option for JL Industries siren strobe model.

JL Industries is an authorized reseller of the HeartSine and LIFEPAK emergency aid specialties indicated.

          - Basis-of-Design: Activar Construction Products Group, Inc. - JL Industries; ["Commander," audible alarm or comparable] [Manufacturer's optional siren strobe].

Alarm Contacts: [14MAG, Magnetic Door Contact] [14RR, Roller Reed Ball Contact] for existing alarm systems.

JL Industries standard AED cabinet identification is a screen-printed graphic.

Identification: Manufacturer's standard warning AED [decal] [screen print graphic].

Finish Color: Powder Coat, White.

EXECUTION

EXAMINATION

        - Examine roughing-in for cabinets to verify actual locations of piping connections before cabinet installation.

Examine walls and partitions for suitable framing depth and blocking where [recessed] [and] [semirecessed] cabinets will be installed.

Proceed with installation only after unsatisfactory conditions have been corrected.

      - PREPARATION

Retain this article if Project includes recessed or semirecessed cabinets.

Prepare recesses for [recessed] [and] [semirecessed] automated external defibrillator cabinets as required by type and size of cabinet and trim style.

INSTALLATION

General: Install automated external defibrillator cabinets in locations and at mounting heights indicated[ or, if not indicated, at height indicated below:][ or, if not indicated, at heights acceptable to authorities having jurisdiction.]

Retain "Automated External Defibrillator Cabinets" Subparagraph below if retaining first option in "General" Paragraph above. If more than one height is required, indicate locations for each height. In rooms required to comply with ADA-ABA Guidelines, mounting height for AED cabinets is not to exceed 48 inches (1219 mm) to the handle.

Automated External Defibrillator Cabinets: [48 inches (1219 mm)] <Insert dimension> above finished floor to top of fire extinguisher.

Automated External Defibrillator Cabinets: Fasten cabinets to structure, square and plumb.

Retain first subparagraph below if default requirement suits Project.

Unless otherwise indicated, provide recessed automated external defibrillator cabinets. If wall thickness is inadequate for recessed cabinets, provide semirecessed automated external defibrillator cabinets.

Provide inside latch and lock for break-glass panels.

Fasten mounting brackets to inside surface of automated external defibrillator cabinets, square and plumb.

Retain this article if decals or vinyl lettering is required.

Identification:

Apply [decals] [vinyl lettering] at locations indicated.

ADJUSTING AND CLEANING

Remove temporary protective coverings and strippable films, if any, as automated external defibrillator cabinets are installed unless otherwise indicated in manufacturer's written installation instructions.

Adjust automated external defibrillator cabinet doors to operate easily without binding. Verify that integral locking devices operate properly.

On completion of automated external defibrillator cabinet installation, clean interior and exterior surfaces as recommended by manufacturer.

Touch up marred finishes or replace automated external defibrillator cabinets that cannot be restored to factory-finished appearance. Use only materials and procedures recommended or furnished by automated external defibrillator cabinet manufacturer.

END OF SECTION 104300