Copyright 2020 by The American Institute of Architects (AIA)

Exclusively published and distributed by Deltek, Inc. for the AIA

This Product MasterSpec Section is licensed by Deltek, Inc. to Activar Construction Products Group, Inc. - JL Industries ("Licensee").

This Product MasterSpec Section modifies the original MasterSpec text and does not include the full content of the original MasterSpec Section.

Revisions made to the original MasterSpec text are made solely by the Licensee and are not endorsed by, or representative of the opinions of, Deltek or The American Institute of Architects (AIA). Neither AIA nor Deltek are liable in any way for such revisions or for the use of this Product MasterSpec Section by any end user. A qualified design professional should review and edit the document to suit project requirements.

For more information, contact Activar Construction Products Group, Inc. - JL Industries, 9702 Newton Ave. S., Bloomington, MN 55431; Phone (800) 554-6077; Website: www.activarcpg.com; Email: sales@activarcpg.com.

For information about MasterSpec, contact Deltek at (800) 424-5080 or visit masterspec.com.

SECTION 083123 - FLOOR DOORS

TIPS:

To view non-printing Editor's Notes that provide guidance for editing, click on MasterWorks/Single-File Formatting/Toggle/Editor's Notes.

To read detailed research, technical information about products and materials, and coordination checklists, click on MasterWorks/Supporting Information.

Access Product MasterSpec Sections:

<Double click here to view the list of manufacturer Sections available at ProductMasterSpec.com.>

Revise this Section by deleting and inserting text to meet Project-specific requirements.

MasterSpec includes provisions for LEED 2009, LEED v4, IgCC, and Green Globes.

GENERAL

SUMMARY

Section Includes:

Aluminum floor doors.

Steel floor doors.

Stainless steel floor doors.

Related Requirements:

Retain subparagraphs below to cross-reference requirements Contractor might expect to find in this Section but are specified in other Sections.

Section 077200 "Roof Accessories" for roof hatches.

Section 078123 "Intumescent Fire Protection" for fire protection applied to underside of fire doors.

Section 083113 "Access Doors and Frames" for wall- and ceiling-mounted access doors and frames.

ACTION SUBMITTALS

Product Data: For each type of product.

Retain option in subparagraph below if fire-rated units are included in the Work.

Include construction details[, fire ratings,] materials, individual components and profiles, and finishes.

Insert requirements for Shop Drawings if custom floor doors are required. Insert requirements for Samples if required by Project.

Product Schedule: For floor doors.[ Use same designations indicated on Drawings.]

Sustainable Design Submittals:

Retain "Product Data" Subparagraph below to require minimum recycled content for LEED 2009, MRc  4 "Recycled Content."

Product Data: For recycled content, indicating postconsumer and preconsumer recycled content and cost.

"Product Certificates" Subparagraph below applies to LEED 2009, Materials and Resources Credit 5, "Regional Materials."

Product Certificates: For regional materials, indicating location of material manufacturer and point of extraction, harvest, or recovery for each raw material. Include distance to Project and cost for each regional material.

Retain "Environmental Product Declaration (EPD)" Subparagraph below for LEED v4 "MRc Building Product Disclosure and Optimization - Environmental Product Declarations." See the Evaluations. Verify, with manufacturer, that EPDs are available for each product.

Environmental Product Declaration (EPD): For each product.

"Product Certificates" Subparagraph below applies to IgCC, which requires that a minimum of 55 percent of building materials or products be extracted, harvested, manufactured, or recovered within 500 miles (800 km) of Project. See IgCC-2012, 505.2.5.

Product Certificates: For indigenous materials, indicating location of material manufacturer and point of extraction, harvest, or recovery for each raw material. Include distance to Project, means of transportation, and cost for each indigenous material.

Retain "Environmental Product Declaration (EPD)" Subparagraph below if products specified in the Section are required to have an EPD to meet the IgCC's requirement of 55 percent recycled materials.

Environmental Product Declaration (EPD): For each product.

"Product Certificates" Subparagraph below applies to ASHRAE 189.1, which requires that a minimum of 15 percent of building materials or products be extracted, harvested, manufactured, or recovered within 500 miles (800 km) of Project. See ASHRAE 189.1-2014, 9.4.1.2.

Product Certificates: For regional materials, indicating location of material manufacturer and point of extraction, harvest, or recovery for each raw material. Include distance to Project, means of transportation, and cost for each regional material.

First "Environmental Product Declaration (EPD)" Subparagraph below applies to ASHRAE 189.1 if products specified in the Section are used to meet the requirements of paragraph 9.4.1.4, "Multiple-Attribute Product Declaration or Certification," which requires EPDs for a minimum of 10 products.

Environmental Product Declaration: For each product.

Subparagraphs below apply to Green Globes v1.4 if products specified in the Section are used to meet the requirements of paragraph 3.5.1.2 "Path B: Prescriptive Path for Building Core and Shell," which requires that a certain percentage of the materials used in the core and shell have EPDs, third-party certifications, and/or third-party life cycle assessments.

Environmental Product Declaration (EPD): For each product.

Third-Party Certifications: For each product.

Third-Party Certified Life Cycle Assessment: For each product.

INFORMATIONAL SUBMITTALS

Coordinate "Qualification Data" Paragraph below with qualification requirements in Section 014000 "Quality Requirements" and as may be supplemented in "Quality Assurance" Article.

Qualification Data: For testing and inspecting agency.

Retain "Fire-Rated Door Inspector" Subparagraph below, or delete and retain second subparagraph below. Certification in second subparagraph below should be acceptable by all authorities having jurisdiction. See the Evaluations.

Fire-Rated Door Inspector: Submit documentation of compliance with NFPA 80, Section 5.2.3.1.

Submit copy of DHI Fire and Egress Door Assembly Inspector (FDAI) certificate.

CLOSEOUT SUBMITTALS

Record Documents: For fire-rated floor doors, list of applicable room name and number in which floor door is located.

QUALITY ASSURANCE

Fire-Rated Door Inspector Qualifications: Inspector for field quality control inspections of fire-rated door assemblies shall meet the qualifications set forth in NFPA 80, Section 5.2.3.1 and the following:

Retain subparagraph below if requiring fire door inspectors to be certified under DHI's certification program. Verify, with authorities having jurisdiction, if other DHI certifications are acceptable, such as Architectural Hardware Consultant (AHC), Certified Door Consultant (CDC), and Architectural Openings Consultant (AOC).

Door and Hardware Institute Fire and Egress Door Assembly Inspector (FDAI) certification.

PRODUCTS

Manufacturers and products listed in this Section are neither recommended nor endorsed by the AIA or Deltek. Before selecting manufacturers and products, verify availability, suitability for intended applications, and compliance with minimum performance requirements. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

Product options commonly available from manufacturers are included in square brackets throughout the Section Text. Not every manufacturer listed can provide every option offered; verify availability with manufacturers. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

PERFORMANCE REQUIREMENTS

Retain "Fire-Rated Floor Doors" Paragraph below if fire-rated units are required.

Fire-Rated Floor Doors: Assemblies complying with NFPA 80 that are listed and labeled by a qualified testing agency in accordance with NFPA 288.

ALUMINUM FLOOR DOORS

Gutter Channel Frame Aluminum Floor Door:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Activar Construction Products Group, Inc. - JL Industries; FLDD with Integral Gutter drainable floor door or comparable product by one of the following:

BILCO Company (The).

Halliday Products.

Williams Bros. Corporation of America (The).

<Insert manufacturer's name>.

Frame: Mill finish aluminum with bituminous coating on outer frame, gutter profile, with 1-1/2 inch (38 mm) FTP integral drainage coupling and perimeter gasket.

Retain second option in "Door" Subparagraph below with 48 by 48 or 60 by 60 inch floor doors.

Door: [Single] [Double] leaf; 1/4-inch- (6.4-mm-) thick, diamond-pattern mill-finish aluminum plate.

Coordinate size locations with drawings.

Door Size(s): [24 by 24 inches (610 by 610 mm)] [24 by 36 inches (610 by 914 mm)] [30 by 30 inches (762 by 762 mm)] [30 by 48 inches (762 by 1219 mm)] [36 by 36 inches (914 by 914 mm)] [36 by 48 inches (914 by 1219 mm)] [37 by 30 inches (940 by 762 mm)] [42 by 42 inches (1067 by 1067 mm)] [48 by 48 inches (1219 by 1219 mm)] [60 by 60 inches (1524 by 1524 mm)].

Manufacturers' offerings for loading capacity vary; confirm availability. See the Evaluations for discussion of AASHTO H20.

Loading Capacity: 300-lbf/sq. ft. (14.4-kN/sq. m) pedestrian live load.

Hardware:

Material and Finish: Type 304 stainless steel, including latch and lifting mechanism assemblies, hold-open arms, and brackets, hinges, pins, and fasteners.

Hinges: Type 304 stainless steel.

Operating Mechanism: Adjustable counterbalancing springs, heavy-duty hold-open arm that automatically locks door open at 90 degrees, release handle with vinyl grip that allows for one-handed closure, and recessed lift handle.

Latch: Hexhead operated, flush removable screwdriver head threaded protection plug.

Lock: [Padlock hasp] [Recessed padlock hasp].

Angle Frame Aluminum Floor Door:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain first option in "Basis-of-Design" Paragraph for new openings; retain second option for retrofits.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Activar Construction Products Group, Inc. - JL Industries; [FLDA] [FLDE] angled floor door or comparable product by one of the following:

BILCO Company (The).

Halliday Products.

Williams Bros. Corporation of America (The).

<Insert manufacturer's name>.

Frame: Mill finish aluminum, angle profile.

Door size 48 by 48-inch is available with a single or double leaf.

Retain second option in "Door" Subparagraph below with 48 by 48 or 60 by 60 inch new angle framed doors.

Door: [Single] [Double] leaf; 1/4-inch- (6.4-mm-) thick, diamond-pattern mill-finish aluminum plate.

Coordinate size locations with drawings.

Select sizes from "Angled Floor Door Size(s)" Subparagraph below with JL Industries model "FLDA" for new angled floor doors; select sizes from "Angled Retrofit Floor Door Size(s)" Subparagrah below with JL Industries model "FLDE" for existing floor door retrofits.

Angled Floor Door Size(s): [24 by 24 inches (610 by 610 mm)] [24 by 36 inches (610 by 914 mm)] [30 by 30 inches (762 by 762 mm)] [30 by 48 inches (762 by 1219 mm)] [36 by 36 inches (914 by 914 mm)] [36 by 48 inches (914 by 1219 mm)] [37 by 30 inches (940 by 762 mm)] [42 by 42 inches (1067 by 1067 mm)] [48 by 48 inches (1219 by 1219 mm)] [60 by 60 inches (1524 by 1524 mm)].

Angled Retrofit Floor Door Size(s) for Retrofit: [23 by 23 inches (584 by 584 mm)] [23 by 35 inches (584 by 889 mm)] [29 by 29 inches (737 by 737 mm)] [29 by 47 inches (737 by 1194 mm)] [35 by 35 inches (889 by 889 mm)] [35 by 47 inches (889 by 1194 mm)] [41 by 41 inches (1041 by 1041 mm)] [47 by 47 inches (1194 by 1194 mm)].

Manufacturers' offerings for loading capacity vary; confirm availability. See the Evaluations for discussion of AASHTO H20.

Loading Capacity: 300-lbf/sq. ft. (14.4-kN/sq. m) pedestrian live load.

Hardware:

Material and Finish: Type 304 stainless steel, including latch and lifting mechanism assemblies, hold-open arms, and brackets, hinges, pins, and fasteners.

Hinges: Type 304 stainless steel.

Operating Mechanism: Type 304 stainless steel gas assist opener, heavy-duty hold-open arm that automatically locks door open at 90 degrees, release handle with vinyl grip that allows for one-handed closure, and recessed lift handle.

Latch: Hex head operated, flush removable screwdriver head threaded protection plug.

Lock: [Padlock hasp] [Recessed padlock hasp].

Recessed Cover Aluminum Floor Door:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Activar Construction Products Group, Inc. - JL Industries; FLDR recessed floor door or comparable product by one of the following:

BILCO Company (The).

Karp Associates, Inc.

Williams Bros. Corporation of America (The).

<Insert manufacturer's name>.

Frame: Mill finish 3/4-inch (6.4-mm) aluminum with 1/8-inch (6.44-mm) lip, angle profile.

Door: Single  leaf; 1/4-inch- (6.4-mm-) thick aluminum plate with 1/8-inch-deep (3.2-mm-deep) recess for application of finish materials.

Coordinate size locations with drawings.

Size(s): [24 by 24 inches (610 by 610 mm)] [30 by 30 inches (762 by 762 mm)] [30 by 36 inches (762 by 914 mm)] [30 by 48 inches (762 by 1219 mm)] [36 by 30 inches (914 by 762 mm)] [36 by 36 inches (914 by 914 mm)] [36 by 48 inches (914 by 1219 mm)] [42 by 42 inches (1067 by 1067 mm)] [42 by 54 inches (1067 by 1372 mm)].

Loading Capacity: 150-lbf/sq. ft. (7.2-kN/sq. m) pedestrian live load.

Hardware:

Material and Finish: Aluminum, mill finish.

Hinges: Aluminum arm-type hinge with Type 304 stainless steel bolt.

Operating Mechanism: Adjustable counterbalancing springs, heavy-duty hold-open arm that automatically locks door open at 90 degrees, release handle with vinyl grip that allows for one-handed closure, and recessed lift handle.

Latch: Zinc-plated steel slam latch with flush key operator on exterior and handle opener on inside.

Revise "Lock" Subparagraph below for other options available; common types are listed.

Lock: [Latch with removable handle] [Recessed padlock hasp] [Recessed padlock hasp with cover] [Keyed deadbolt lock] [Keyed deadbolt lock with threaded protection plug] [Hasp and staple] <Insert lock type>.

Fire-Rated Aluminum Floor Door:

Retain "Manufacturers" Subparagraph below and list of manufacturers to require products from manufacturers listed or a comparable product from other manufacturers.

Manufacturers: Subject to compliance with requirements, provide products by one of the following:

Acudor Products, Inc.

Babcock-Davis.

Maxam Metal Products Limited.

Nystrom.

U.S.F. Fabrication.

Williams Bros. Corporation of America (The).

<Insert manufacturer's name>.

Frame: Mill finish aluminum, angle profile.

Door: Single leaf; 1/4-inch- (6.4-mm-) thick, [diamond-pattern] [smooth] mill-finish aluminum plate; with manufacturer's standard heat-resistant insulation and fire-rated gasket.

Manufacturers' offerings for loading capacity vary; confirm availability.

Loading Capacity: [150-lbf/sq. ft. (7.2-kN/sq. m)] [300-lbf/sq. ft. (14.4-kN/sq. m)] pedestrian live load.

Insulation: [Manufacturer's standard] [Fiberglass] [Urethane], with liner pan.

Hardware:

Material and Finish: [Manufacturer's standard] [Type 316 stainless steel, including latch and lifting mechanism assemblies, hold-open arms, and brackets, hinges, pins, and fasteners].

Hinges: Heavy-duty butt hinges with stainless steel pins.

Operating Mechanism: Heavy-duty hold-open arm that automatically locks door open at 90 degrees with fusible-link to automatically close door in event of fire, release handle with vinyl grip that allows for one-handed closure, adjustable counterbalancing springs, and recessed lift handle.

Latch: Stainless steel slam latch.

Lock: [Latch with removable handle] [Recessed padlock hasp] [Recessed padlock hasp with cover] [Keyed deadbolt lock] [Keyed deadbolt lock with threaded protection plug] [Hasp and staple] <Insert lock type>.

Fire-Resistance Rating: Not less than [that indicated] [that of adjacent construction] [1 hour] [1-1/2 hours] [2 hours] [3 hours] <Insert requirement>.

Fire-Rated Recessed Cover Aluminum Floor Door:

Retain "Manufacturers" Subparagraph below and list of manufacturers to require products from manufacturers listed or a comparable product from other manufacturers.

Manufacturers: Subject to compliance with requirements, provide products by one of the following:

Babcock-Davis.

BILCO Company (The).

Maxam Metal Products Limited.

Nystrom.

U.S.F. Fabrication.

Williams Bros. Corporation of America (The).

<Insert manufacturer's name>.

Frame: Mill finish aluminum, angle profile.

Door: Single leaf; 1/4-inch-thick (6.4-mm-thick) aluminum plate with [1/8-inch-deep (3.2-mm-deep)] [3/16-inch-deep (4.8-mm-deep)] [1-inch-deep (25.4-mm-deep)] recess for application of finish materials.

Loading Capacity: [150-lbf/sq. ft. (7.2-kN/sq. m)] [300-lbf/sq. ft. (14.4-kN/sq. m)] pedestrian live load.

Insulation: [Manufacturer's standard] [Fiberglass] [Urethane], with liner pan.

Hardware:

Material and Finish: [Manufacturer's standard] [Type 316 stainless steel, including latch and lifting mechanism assemblies, hold-open arms, and brackets, hinges, pins, and fasteners].

Hinges: Heavy-duty butt hinges with stainless steel pins.

Operating Mechanism: Heavy-duty hold-open arm that automatically locks door open at 90 degrees with fusible-link to automatically close door in event of fire, release handle with vinyl grip that allows for one-handed closure, adjustable counterbalancing springs, and recessed lift handle.

Latch: Stainless steel slam latch.

Lock: [Latch with removable handle] [Recessed padlock hasp] [Recessed padlock hasp with cover] [Keyed deadbolt lock] [Keyed deadbolt lock with threaded protection plug] [Hasp and staple] <Insert lock type>.

Fire-Resistance Rating: Not less than [that indicated] [that of adjacent construction] [1 hour] [1-1/2 hours] [2 hours] [3 hours] <Insert requirement>.

Revise "Safety Accessories" Paragraph below if required by authorities having jurisdiction; delete below if not required.

Safety Accessories: Safety [chains] [net] [railing] [telescoping safety post] [grid] <Insert safety device>.

STEEL FLOOR DOORS

Fire-Rated Steel Floor Door:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Activar Construction Products Group, Inc. - JL Industries; [FFD1, 1-hour] [FFD2, 2-hour] [FFD3, 3-hour] fire-rated floor door or comparable product by one of the following:

Maxam Metal Products Limited.

U.S.F. Fabrication.

<Insert manufacturer's name>.

Frame: [Prime-painted] [Hot-dip galvanized] steel, angle profile. Bituminous coating on outer frame.

Retain first "Door" Subparagraph below for JL Industries standard rated steel door panels; retain second subparagraph for optional aluminum plate door panels.

Door: Single leaf 3/16-inch-thick (4.8-mm-thick), diamond pattern; [prime-painted] [hot-dip galvanized] steel plate with 14 gage mill finish aluminum liner; with manufacturer's standard heat-resistant insulation; and fire-rated gasketing on all four sides of upper frame section.

Door: Single leaf 1/4-inch-thick (6.3-mm-thick), diamond pattern; mill finish aluminum plate with bituminous coating on outer frame; with manufacturer's standard heat-resistant insulation; and fire-rated gasketing on all four sides of upper frame section.

Coordinate size locations with drawings.

JL Industries 3-hour rated doors are available in 48 by 48 and 60 by 60-inch sizes in addition to the options in "Door Size(s)" Subparagraph below.

Door Size(s): [24 by 24 inches (610 by 610 mm)] [24 by 36 inches (610 by 914 mm)] [30 by 30 inches (762 by 762 mm)] [30 by 48 inches (762 by 1219 mm)] [36 by 36 inches (914 by 914 mm)] [36 by 48 inches (914 by 1219 mm)] [36 by 30 inches (914 by 762 mm)] [42 by 54 inches (1067 by 1372 mm)] [42 by 42 inches (1067 by 1067 mm)].

Manufacturers' offerings for loading capacity vary; confirm availability.

Loading Capacity: 150-lbf/sq. ft. (7.2-kN/sq. m) pedestrian live load.

Insulation: Manufacturer's standard, with liner pan.

Hardware:

Material and Finish: Type 316 stainless steel, including latch and lifting mechanism assemblies, hold-open arms, and brackets, hinges, pins, and fasteners.

Hinges: Continuous stainless steel piano hinge.

Operating Mechanism: Type 316 stainless steel nitrogen cylinders..

Latch: Stainless steel slam latch with removable cover plug.

Lock: [Recessed turn handle] [Recessed topside turn handle with underside detention lock] [Padlock hasp].

Options: [Self-closing mechanism] [Fusible link activates at 165 deg F (73 deg C), 300 lb/sq. ft. (136 kg/sq. m) live load].

Coordinate rating options in "Fire-Resistance Rating" Subparagraph below with JL Industries basis-of-design product selection.

Fire-Resistance Rating: Not less than [1 hour] [2 hours] [3 hours].

Gutter Channel Frame Steel Floor Door:

Retain "Manufacturers" Subparagraph and list of manufacturers below to require products from manufacturers listed or a comparable product from other manufacturers.

Manufacturers: Subject to compliance with requirements, provide products by one of the following:

Babcock-Davis.

BILCO Company (The).

Nystrom.

U.S.F. Fabrication.

<Insert manufacturer's name>.

Frame: [Prime-painted] [Hot-dip galvanized] steel, gutter profile, with integral drainage coupling and perimeter gasket.

Generally, retain same material for door in "Door" Subparagraph below as retained in "Frame" Subparagraph above. Some manufacturers offer different materials for doors and frames. Verify availability of thicknesses with manufacturers.

Door: [Single] [Double] leaf; [manufacturer's standard thickness] [3/16- or 1/4-inch-thick (4.8-mm- or 6.4-mm-thick)] [3/16-inch-thick (4.8-mm-thick)] [1/4-inch-thick (6.4-mm-thick)], [diamond pattern] [smooth]; [prime-painted] [hot-dip galvanized] steel plate.

Manufacturers' offerings for loading capacity vary; confirm availability. See the Evaluations for discussion of AASHTO H20.

Loading Capacity: [150-lbf/sq. ft. (7.2-kN/sq. m) pedestrian live load] [300-lbf/sq. ft. (14.4-kN/sq. m) pedestrian live load] [AASHTO H20 concentrated wheel load].

Options: [Debris gasket] [Odor gasket] <Insert option>.

Hardware:

Material and Finish: [Manufacturer's standard] [Type 316 stainless steel, including latch and lifting mechanism assemblies, hold-open arms, and brackets, hinges, pins, and fasteners].

Hinges: Heavy-duty butt hinges with stainless steel pins.

Operating Mechanism: Adjustable counterbalancing springs, heavy-duty hold-open arm that automatically locks door open at 90 degrees, release handle with vinyl grip that allows for one-handed closure, and recessed lift handle.

Latch: Stainless steel slam latch.

Revise "Lock" Subparagraph below for other options available; common types are listed.

Lock: [Latch with removable handle] [Recessed padlock hasp] [Recessed padlock hasp with cover] [Keyed deadbolt lock] [Keyed deadbolt lock with threaded protection plug] [Hasp and staple] <Insert lock type>.

Angle Frame Steel Floor Door:

Retain "Manufacturers" Subparagraph and list of manufacturers below to require products from manufacturers listed or a comparable product from other manufacturers.

Manufacturers: Subject to compliance with requirements, provide products by one of the following:

BILCO Company (The).

MIFAB, Inc.

Milcor; a division of Hart & Cooley, Inc.

U.S.F. Fabrication.

Williams Bros. Corporation of America (The).

<Insert manufacturer's name>.

Frame: [Prime-painted] [Hot-dip galvanized] [Stainless] steel, angle profile.

Generally, retain same material for door in "Door" Subparagraph below as retained in "Frame" Subparagraph above. Some manufacturers offer different materials for doors and frames. Verify availability of thicknesses with manufacturers.

Door: [Single] [Double] leaf; [manufacturer's standard thickness] [3/16- or 1/4-inch-thick (4.8-mm- or 6.4-mm-thick)] [3/16-inch-thick (4.8-mm-thick)] [1/4-inch-thick (6.4-mm-thick)], [diamond pattern] [smooth]; [prime-painted] [hot-dip galvanized] steel plate.

Manufacturers' offerings for loading capacity vary; confirm availability. See the Evaluations for discussion of AASHTO H20.

Loading Capacity: [150-lbf/sq. ft. (7.2-kN/sq. m) pedestrian live load] [300-lbf/sq. ft. (14.4-kN/sq. m) pedestrian live load] [AASHTO H20 concentrated wheel load].

Options: [Debris gasket] [Odor gasket] <Insert option>.

Hardware:

Material and Finish: [Manufacturer's standard] [Type 316 stainless steel, including latch and lifting mechanism assemblies, hold-open arms, and brackets, hinges, pins, and fasteners].

Hinges: Heavy-duty butt hinges with stainless steel pins.

Operating Mechanism: Adjustable counterbalancing springs, heavy-duty hold-open arm that automatically locks door open at 90 degrees, release handle with vinyl grip that allows for one-handed closure, and recessed lift handle.

Latch: Stainless steel slam latch.

Revise "Lock" Subparagraph below for other options available; common types are listed.

Lock: [Recessed turn handle] [Recessed topside turn handle with underside detention lock] [Padlock hasp].

STAINLESS STEEL FLOOR DOORS

Gutter Channel Frame Stainless Steel Floor Door:

Retain "Manufacturers" Subparagraph and list of manufacturers below to require products from manufacturers listed or a comparable product from other manufacturers.

Manufacturers: Subject to compliance with requirements, provide products by one of the following:

Babcock-Davis.

Nystrom.

U.S.F. Fabrication.

<Insert manufacturer's name>.

Retain the more expensive "Type 316" option in "Frame" and "Door" subparagraphs below for more corrosion resistance.

Frame: [Type 304] [Type 316] stainless steel, gutter profile, with integral drainage coupling and perimeter gasket.

Generally, retain same material for door in "Door" Subparagraph below as retained in "Frame" Subparagraph above. Some manufacturers offer different materials for doors and frames. Verify availability of thicknesses with manufacturers.

Door: [Single] [Double] leaf; [manufacturer's standard thickness] [3/16- or 1/4-inch-thick (4.8-mm- or 6.4-mm-thick)] [3/16-inch-thick (4.8-mm-thick)] [1/4-inch-thick (6.4-mm-thick)], [diamond pattern] [smooth], [Type 304] [Type 316] stainless steel plate.

Manufacturers' offerings for loading capacity vary; confirm availability. See the Evaluations for discussion of AASHTO H20.

Loading Capacity: [150-lbf/sq. ft. (7.2-kN/sq. m) pedestrian live load] [300-lbf/sq. ft. (14.4-kN/sq. m) pedestrian live load] [AASHTO H20 concentrated wheel load].

Options: [Debris gasket] [Odor gasket] <Insert option>.

Hardware:

Material and Finish: [Manufacturer's standard] [Type 316 stainless steel, including latch and lifting mechanism assemblies, hold-open arms, and brackets, hinges, pins, and fasteners].

Hinges: Heavy-duty butt hinges with stainless steel pins.

Operating Mechanism: Adjustable counterbalancing springs, heavy-duty hold-open arm that automatically locks door open at 90 degrees, release handle with vinyl grip that allows for one-handed closure, and recessed lift handle.

Latch: Stainless steel slam latch.

Revise "Lock" Subparagraph below for other options available; common types are listed.

Lock: [Latch with removable handle] [Recessed padlock hasp] [Recessed padlock hasp with cover] [Keyed deadbolt lock] [Keyed deadbolt lock with threaded protection plug] [Hasp and staple] <Insert lock type>.

Angle Frame Stainless Steel Floor Door:

Retain "Manufacturers" Subparagraph and list of manufacturers below to require products from manufacturers listed or a comparable product from other manufacturers.

Manufacturers: Subject to compliance with requirements, provide products by the following:

U.S.F. Fabrication.

<Insert manufacturer's name>.

Retain the more expensive "Type 316" option in "Frame" and "Door" subparagraphs below for more corrosion resistance.

Frame: [Type 304] [Type 316] stainless steel, angle profile.

Generally, retain same material for door in "Door" Subparagraph below as retained in "Frame" Subparagraph above. Some manufacturers offer different materials for doors and frames. Verify availability of thicknesses with manufacturers.

Door: [Single] [Double] leaf; [manufacturer's standard thickness] [3/16- or 1/4-inch-thick (4.8-mm- or 6.4-mm-thick)] [3/16-inch-thick (4.8-mm-thick)] [1/4-inch-thick (6.4-mm-thick)], [diamond pattern] [smooth], [Type 304] [Type 316] stainless steel plate.

Manufacturers' offerings for loading capacity vary; confirm availability. See the Evaluations for discussion of AASHTO H20.

Loading Capacity: [150-lbf/sq. ft. (7.2-kN/sq. m) pedestrian live load] [300-lbf/sq. ft. (14.4-kN/sq. m) pedestrian live load] [AASHTO H20 concentrated wheel load].

Options: [Debris gasket] [Odor gasket] <Insert option>.

Hardware:

Material and Finish: [Manufacturer's standard] [Type 316 stainless steel, including latch and lifting mechanism assemblies, hold-open arms, and brackets, hinges, pins, and fasteners].

Hinges: Heavy-duty butt hinges with stainless steel pins.

Operating Mechanism: Adjustable counterbalancing springs, heavy-duty hold-open arm that automatically locks door open at 90 degrees, release handle with vinyl grip that allows for one-handed closure, and recessed lift handle.

Latch: Stainless steel slam latch.

Revise "Lock" Subparagraph below for other options available; common types are listed.

Lock: [Latch with removable handle] [Recessed padlock hasp] [Recessed padlock hasp with cover] [Keyed deadbolt lock] [Keyed deadbolt lock with threaded protection plug] [Hasp and staple] <Insert lock type>.

Fire-Rated Stainless Steel Floor Door:

Retain "Manufacturers" Subparagraph and list of manufacturers below to require products from manufacturers listed or a comparable product from other manufacturers.

Manufacturers: Subject to compliance with requirements, provide products by the following:

<Insert manufacturer's name>.

Retain the more expensive "Type 316" option in "Frame" and "Door" Paragraphs below for more corrosion resistance.

Frame: [Type 304] [Type 316] stainless steel, angle profile.

Generally, retain same material for door in "Door" Subparagraph below as retained in "Frame" Subparagraph above. Some manufacturers offer different materials for doors and frames. Verify availability of thicknesses with manufacturers.

Door: [Single] [Double] leaf; [manufacturer's standard thickness] [3/16- or 1/4-inch-thick (4.8-mm- or 6.4-mm-thick)] [3/16-inch-thick (4.8-mm-thick)] [1/4-inch-thick (6.4-mm-thick)], [diamond pattern] [smooth], [Type 304] [Type 316] stainless steel plate; with manufacturer's standard heat-resistant insulation and fire-rated gasket.

Manufacturers' offerings for loading capacity vary; confirm availability.

Loading Capacity: [150-lbf/sq. ft. (7.2-kN/sq. m)] [300-lbf/sq. ft. (14.4-kN/sq. m)] pedestrian live load.

Insulation: [Manufacturer's standard] [Fiberglass] [Urethane], with liner pan.

Hardware:

Material and Finish: [Manufacturer's standard] [Type 316 stainless steel, including latch and lifting mechanism assemblies, hold-open arms, and brackets, hinges, pins, and fasteners].

Hinges: Heavy-duty butt hinges with stainless steel pins.

Operating Mechanism: Heavy-duty hold-open arm that automatically locks door open at 90 degrees with fusible-link to automatically close door in event of fire, release handle with vinyl grip that allows for one-handed closure, adjustable counterbalancing springs, and recessed lift handle.

Latch: Stainless steel slam latch.

Lock: [Latch with removable handle] [Recessed padlock hasp] [Recessed padlock hasp with cover] [Keyed deadbolt lock] [Keyed deadbolt lock with threaded protection plug] [Hasp and staple] <Insert lock type>.

Fire-Resistance Rating: Not less than [that indicated] [that of adjacent construction] [45 minutes] [1 hour] [1-1/2 hours] [2 hours] [3 hours] <Insert requirement>.

Revise "Safety Accessories" Paragraph below if required by authorities having jurisdiction; delete below if not required.

Safety Accessories: Safety [chains] [net] [railing] [telescoping safety post] [grid] <Insert safety device>.

MATERIALS

Retain "Recycled Content of Steel Products" Paragraph below to specify recycled content if required. An alternative method of requiring recycled content is to retain requirement in Project's Division 01 sustainable design requirements Section that gives Contractor the option and responsibility to determine how recycled content requirements will be met.

Recycled Content of Steel Products: Postconsumer recycled content plus one-half of preconsumer recycled content not less than [25] <Insert number> percent.

Retain materials in this article or revise to suit Project.

Steel Plates, Shapes, and Bars: ASTM A36/A36M.

"Rolled-Steel Floor Plate" Paragraph below specifies minimum yield point of 30 ksi (205 MPa); revise if a higher strength is required.

Rolled-Steel Floor Plate: ASTM A786/A786M, rolled from plate complying with ASTM A36/A36M or ASTM A283/A283M, Grade C or D.

Steel Sheet: Uncoated or electrolytic zinc coated, ASTM A879/A879M, with cold-rolled steel sheet substrate complying with ASTM A1008/A1008M, Commercial Steel (CS), exposed.

Retain "Metallic-Coated Steel Sheet" Paragraph below with JL Industries galvannealed steel floor door products.

Metallic-Coated Steel Sheet: ASTM A653/A653M, Commercial Steel (CS), Type B; with minimum G60 (Z180) or A60 (ZF180) metallic coating.

Rolled-Stainless Steel Floor Plate: ASTM A793, manufacturer's standard finish.

Stainless Steel Sheet, Strip, Plate, and Flat Bars: ASTM A666. Remove tool and die marks and stretch lines, or blend into finish.

Aluminum Extrusions: ASTM B221 (ASTM B221M), Alloy 6063-T6.

Aluminum-Alloy Rolled Tread Plate: ASTM B632/B632M, Alloy 6061-T6.

Aluminum Sheet: ASTM B209 (ASTM B209M), alloy and temper recommended by aluminum producer and finisher for type of use and finish indicated.

Frame Anchors: Same material as door face.

Inserts, Bolts, and Anchor Fasteners: Hot-dip galvanized steel in accordance with ASTM A153/A153M or ASTM F2329.

FABRICATION

General: Provide floor doors manufactured as integral units ready for installation.

Metal Surfaces: For metal surfaces exposed to view in the completed Work, provide materials with smooth, flat surfaces without blemishes. Do not use materials with exposed pitting, seam marks, roller marks, rolled trade names, or roughness.

Grind exposed welds smooth and flush with adjacent surfaces. Furnish attachment devices and fasteners of type required to secure floor doors to types of supports indicated.

Latching Mechanisms: Furnish number required to hold doors in flush, smooth plane when closed.

For cylinder locks, furnish two keys per lock and key all locks alike.

For recessed panel doors, provide access sleeves for each locking device. Furnish plastic grommets and install in holes cut through finish.

Retain "Aluminum" Paragraph below for aluminum floor doors.

Aluminum: After fabrication, apply manufacturer's standard protective coating on aluminum that comes in contact with concrete.

FINISHES

Comply with NAAMM's "Metal Finishes Manual for Architectural and Metal Products" for recommendations for applying and designating finishes.

Protect mechanical finishes on exposed surfaces from damage by applying a strippable, temporary protective covering before shipping.

Appearance of Finished Work: Noticeable variations in same piece are not acceptable. Variations in appearance of adjoining components are acceptable if they are within the range of approved Samples and are assembled or installed to minimize contrast.

Hot-dip galvanize items as indicated to comply with ASTM A153/A153M for steel and iron hardware and with ASTM A123/A123M for other steel and iron products.

Retain "Prime Painted Steel" Paragraph below with JL Industries galvannealed steel floor door products.

Prime Painted Steel: Apply manufacturer's standard, lead- and chromate-free, universal primer immediately after surface preparation and pretreatment.

Stainless Steel Finish: Bright, cold-rolled, unpolished ASTM A480/A480M No. 2B finish.

EXECUTION

EXAMINATION

Examine substrates for compliance with requirements for installation tolerances and other conditions affecting performance of the Work.

Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION, GENERAL

Comply with manufacturer's written instructions for installing floor doors.

Retain paragraph below for fire-rated floor doors if required by manufacturer.

Apply intumescent fire protection to underside of floor door cover to minimum thickness required by intumescent fire protection manufacturer for fire rating indicated.

FIELD QUALITY CONTROL

Retaining second option in "Inspection Agency" Paragraph below is typical. If retaining second option in "Inspection Agency" Paragraph, retain "Field quality-control reports" Paragraph in "Informational Submittals."

Inspection Agency: [Owner will engage] [Engage] a qualified inspector to perform inspections and to furnish reports to Architect.

Inspections:

Fire-Rated Door Inspections: Inspect each fire-rated floor door in accordance with NFPA 80, Section 5.2.

Repair or remove and replace installations where inspections indicate that they do not comply with specified requirements.

Reinspect repaired or replaced installations to determine if replaced or repaired door assembly installations comply with specified requirements.

Prepare and submit separate inspection report for each fire-rated floor door indicating compliance with each item listed in [NFPA 80] [and] [NFPA 101].

ADJUSTING

Adjust doors and hardware, after installation, for proper operation.

END OF SECTION 083123